- Turn on the JVC MiniDV/HDD/DVD deck and the TV monitor.

- Press “DV/HDD/DVD” until the green light is underneath “DV” on the deck.

- Load your MiniDV tape into the deck. The TV monitor should display a live connection--if you press play, you should see your video on the monitor.  If not:

  - An RCA A/V cable should run from “DV/HDD/DVD Output” in the back of the miniDV/HD/DVD deck to “Video 1 in” in the back of the TV.

  - The TV’s input should be set to “Video 1”. Press “Input” on the Sharp TV remote to toggle between the inputs.

  - Once a live connection with the TV monitor is achieved, you can continue.

- Use the remote to cue the miniDV tape to the point you want to begin recording footage.  When you find this point, press stop.

- Insert a blank DVD±R/RW into the DVD tray by pressing the eject button on the right-hand side of the panel.

- Press “Input Select,” which is on the left-hand side of the front panel, until it is set to “DV”.

- Press the “Dubbing” button on the remote (very bottom of remote).

  - Use the arrow keys on the remote to select (“DV --> DVD”), then press enter.

  - Select “Manual” to dub a portion of the MiniDV tape and press enter.

  - Press enter on “Select Recording Mode” to choose the video quality of the recording. XP offers the best picture quality, but least amount of recording time (1 hour); EP offers moderate picture quality, but the most amount of time (6 hours).

  - Select “Confirm” on the menu by using the down arrow on the remote.

  - Select “Execute” and press enter.  The miniDV tape will begin recording to the DVD at the point previously selected in step #4.

  - When the portion of the miniDV tape you want recorded has finished, press “stop” and use the selection keys on the remote to select “cancel” and press “enter” to confirm.

  - Finalizing the disc will be necessary for the DVD to be played back on any DVD-player other than this deck.

- To finalize the disc, press “DVD” on the remote so that the DVD lamp lights up on the front panel.

- Press “Set Up” (small, round button on bottom right) on the remote to access the Main Menu screen.

- Use the arrow keys on the remote to select the tabs “HDD/DVD Set up” > “Disc Set Up” > “Finalize” by pressing “      ”  to get to the “Finalize” icon.

- Press “Enter” on the remote to begin finalization, select “OK” and press “Enter.”

- Once the disc has completed finalizing, press “Enter” and eject the DVD from the deck.